Red Hat Identity Management
Client Installation and Configuration

Version 1.1

Version History

Version Number	Date	Author	Summary of Changes
1.0	5/1/2015	Dan Rohr	Initial draft
1.1	8/3/2015	Dan Rohr	Formatting Updates

Table of Contents

# Introduction

## Installation and Configuration Overview

Red Hat Identity Management (IdM) will provide a centralized single pane of glass control for all RHEL systems. In order to get a client bound to the IdM server there are some initial configuration changes, software packages that need to be installed, and finally running the client install.
- Configure the hostname
- Configuring the DNS resolution
- Installing the client
All configuration examples in the following sections will be based on the following information and will need to adjusted accordingly based upon the network environment:
- AD Domain: example.com
- Linux Doamin: linux.example.com
- DC: dc01.example.com
- IdM Server: idm01.linux.example.com

# Hostname and DNS Configuration

## Hostname Configuration
To configure the hostname to properly reflect the Linux domain:

Hostname:
- #hostname
- Should return server1.linux.example.com
- If not then
- #hostname server1.linux.example.com
/etc/sysconfig/network:
- #vim /etc/sysconfig/network
- NETWORKING=yes
- HOSTNAME=server1.linux.example.com
- GATEWAY=<local gateway>
- Save the file
/etc/resolv.conf:
- #vim /etc/resolv.conf
- domain linux.example.com
- search linux.example.com
- nameserver <ip of idm01 server>
- Save the file
At this point it is recommended to log off and log back on so all hostname information properly updates for the session when joining to the IdM domain.
## Install the IPA Client Software
To join the domain you will need to install the IdM client:
#yum -y install ipa-client

# Joining the System to the IdM Domain

## Joining the IdM Domain

In order to join the system to the domain run the following command:
- #ipa-client-install --mkhomedir
- Verify the information and then type yes to continue installing
- When asked for credentials you use an account that is a member of admins group on IdM
- Enter that users password
- Let it run through all the configurations and verify it completes successfully
- Log off and log back in with an user that is in the IdM user store
## Potential Issue
Once the system is joined to the IdM domain it is possible that when a login is attempted it will fail. This can occur even if the joining to the IdM domain was successful. This general happens due to the way the /etc/pam.d/system-auth file is handled. Some system are doing a symbolic link of the /etc/pam.d/system-auth-ac -> /etc/pam.d/system-auth-local instead of just /etc/pam.d/system-auth. It will be necessary to fix this by recreating the symbolic link to the correct file as follows:
- #ln -sf /etc/pam.d/system-auth-ac /etc/pam.d/system-auth
- Close all open ssh sessions and try the login again as changes to pam are immediate